## Slide 1: Amateur Extra Licensing Class
Presented by
W5YI
Arlington, Texas
Antennas
Notes: <number>

## Slide 2: Amateur Radio Extra Class Element 4 Course Presentation
ELEMENT 4 Groupings
  Rules & Regs
  Skywaves & Contesting
  Outer Space Comms
  Visuals & Video Modes
  Digital Excitement with Computers & Radios
  Modulate Your Transmitters
  Amps & Power Supplies
  Receivers with Great Filters

## Slide 3: Amateur Radio Extra Class Element 4 Course Presentation
ELEMENT 4 Groupings
  Oscillate & Synthesize This!
  Circuits & Resonance for All!
  Components in Your New Rig
  Logically Speaking of Counters
  Optops & OpAmps Plus Solar
  Test Gear, Testing, Testing 1,2,3
  Antennas
  Feedlines & Safety

## Slide 4: Amateur Radio Extra Class Antennas
E9A16… The radiation resistance of an antenna is the value of a resistance that would dissipate the same amount of power as that radiated from an antenna.
E9A05… Antenna height and conductor length/diameter ratio, and location of nearby conductive objects determine the radiation resistance of an antenna.
E9A06… The term for the ratio of the radiation resistance of an antenna to the total resistance of the system is antenna efficiency.
Efficiency = (RR/RT) x 100%
RR = Radiation Resistance
RT = Total Resistance

## Slide 5: Amateur Radio Extra Class Antennas
E9A07… Radiation resistance plus ohmic resistance are included in the total resistance of an antenna system.
E9A11… Antenna efficiency is calculated by the equation:
    (radiation resistance / total resistance) x 100%.
Can also be calculated by the equation:
Efficiency = Radiated Power / Input power
E9B01… The orientation of its electric field (E Field) determines the free-space polarization of an antenna.

## Slide 6: Amateur Radio Extra Class Antennas
Propagating Electromagnetic Waves
Electric Field
Magnetic Field
Vertical Polarization

## Slide 7: Amateur Radio Extra Class Antennas
E9A12… The efficiency of an HF quarter-wave grounded vertical antenna can be improved by installing a good radial system.
E9A13… Soil conductivity is the most important factor in determining ground losses for a ground-mounted vertical antenna operating in the 3-30 MHz range.
E9C15… The conductivity and dielectric constant of the soil in the area of the antenna strongly affects the shape of the far-field, low-angle elevation pattern of a vertically polarized antenna.

## Slide 8: Amateur Radio Extra Class Antennas
E9C12… When a vertically polarized antenna is mounted over seawater versus rocky ground the far-field elevation pattern low-angle radiation increases.
E9C17… The main effect of placing a vertical antenna over an imperfect ground is that it reduces low-angle radiation.
E9D14… A thin, flat copper strap several inches wide would be best for minimizing losses in a station's RF ground system.
The thin copper strap will have lower inductive reactance making it a lower loss to the earth ground point.
A lower angle of radiation means longer skip.

## Slide 9: Amateur Radio Extra Class Antennas
E9D15… A connection to 3 or 4 interconnected ground rods driven into the earth would provide the best RF ground for your station.
Copper bonded ground rods
Tower groundedwith three 8’ ground rods

## Slide 10: Amateur Radio Extra Class Antennas
E9C01… The radiation pattern of two 1/4-wavelength vertical antennas spaced 1/2-wavelength apart and fed 180 degrees out of phase is a figure-8 oriented along the axis of the array.
E9C02… The radiation pattern of two 1/4-wavelength vertical antennas spaced 1/4-wavelength apart and fed 90 degrees out of phase is a cardioid.
Two vertical ¼ wave antennas
Feed points180º out of phase
½ wavelength apart
Two ¼ wavelength verticals
¼ wavelength apart with
Feed points 90º out of phase

## Slide 11: Amateur Radio Extra Class Antennas
E9C03… The radiation pattern of two 1/4-wavelength vertical antennas spaced 1/2-wavelength apart and fed in phase is a figure-8 broadside to the axis of the array.
E9A08… A dipole constructed from one wavelength of wire forming a very thin loop is a folded dipole antenna.
Two 1/4 wavelength verticals
1/2 wavelength apart,
feed points in phase
Folded Dipole Antenna Made from 300 Ohm Twin-Lead

## Slide 12: Amateur Radio Extra Class Antennas
E9D10… The approximate feed-point impedance at the center of a folded dipole antenna is 300 ohms.
E9A04… One needs to know the feed point impedance of an antenna to match impedances for maximum power transfer from a feed line.
E9A01… An isotropic Antenna is a theoretical antenna used as a reference for antenna gain.
An isotropic source radiates equally in all directions
Isotropic Radiator Pattern

## Slide 13: Amateur Radio Extra Class Antennas
E9A03… An Isotropic antenna has no (zero) gain in any direction.
E9A02… A 1/2-wavelength dipole has 2.15 dB gain compared to an isotropic antenna.
E9A14… If an antenna has 3.85 dB gain over a 1/2-wavelength dipole then it has 6 dB gain over an isotropic antenna.
The gain over isotropic source for an antenna with a 3.85 dB gain over a dipole antenna would be an additional 2.14 dB of gain.
Remember dipole gain over an isotropic source is 2.14 dB
3.85 dB +1.14dB
= 5.99dB
(Actually 2.14 dB gain, the test question answer is rounded to 2.15 dB)

## Slide 14: Amateur Radio Extra Class Antennas
E9A15… An antenna has 9.85 dB of gain
E9D11… A loading coil is often used with an HF mobile antenna to cancel capacitive reactance.
E9D08… The bandwidth of an antenna is decreased as it is shortened through the use of loading coils.
Remember that a dipole has 2.14 dB of gain as referenced to an isotropic antenna.
12 dB - 2.14 dB
gain =9.86dB
over a 1/2-wavelength dipole
when it has 12 dB of gain over an isotropic antenna.

## Slide 15: Amateur Radio Extra Class Antennas
E9A10… Antenna bandwidth is the frequency range over which an antenna satisfies a performance requirement.
E9D06… An HF mobile antenna loading coil should have a high ratio of reactance to resistance to minimize losses.
E9D05… For a shortened vertical antenna, a loading coil is placed near the center of the vertical radiator to minimize losses and produce the most effective performance.
E9D09… An advantage of using top loading in a shortened HF vertical antenna is improved radiation efficiency.
Performance examples would be – Gain - SWR or impedance - Beam width - etc

## Slide 16: Amateur Radio Extra Class Antennas
E9D13… The resistance decreases and the capacitive reactance increases at the base feed-point of a fixed-length HF mobile antenna as the frequency of operation is lowered.
E9D12… An advantage of using a trapped antenna is that it may be used for multi-band operation.
E9D07… A disadvantage of using a multi-band trapped antenna is that it might radiate harmonics.
Schematic of trap antenna

## Slide 17: Amateur Radio Extra Class Antennas
E9B09… You can approximate beamwidth of a directional antenna by noting the two points where the signal strength of the antenna is 3 dB less than maximum and compute the angular difference.
E9B10… The “Method of Moments” computer program technique is commonly used for modeling antennas.

## Slide 18: Amateur Radio Extra Class Antennas
E9B14… The abbreviation NEC stands for Numerical Electromagnetics Code when applied to antenna modeling programs.
E9B13… The disadvantage of NEC-based antenna modeling programs is that computing time increases as the number of wire segments is increased.
E9B12… The disadvantage of decreasing the number of wire segments in an antenna model below the guideline of 10 segments per half-wavelength is that the computed feed-point impedance may be incorrect.
E9B15… SWR vs. frequency charts, polar plots of the far-field elevation and azimuth patterns, and antenna gain can be obtained by submitting (entering) the details of a proposed new antenna to a modeling program.

## Slide 19: Amateur Radio Extra Class Antennas
E0A01… The difference between the radiation produced by radioactive materials and the electromagnetic energy radiated by an antenna is that RF radiation does not have sufficient energy to break apart atoms and molecules. Radiation, from radioactive sources does.
E0A09… Beryllium Oxide, an insulating material commonly used as a thermal conductor for some types of electronic devices, is extremely toxic if broken or crushed and the particles are accidentally inhaled.
E9B11… The principle that the “Method of Moments” analysis is based on is a wire that is modeled as a series of segments, each having a distinct value of current.
E9A09… Antenna gain is the numerical ratio relating the radiated signal strength of an antenna in the direction of maximum radiation to that of a reference antenna.
Gain is generally expressed in dB relative to either an Isotropic source or a dipole.

## Slide 20: Amateur Radio Extra Class Antennas
E0A07… The "far-field" zone of an antenna is the area where the shape of the antenna pattern is independent of distance.
E9B02… In the antenna radiation pattern shown in Figure E9-1, the 3-dB beamwidth is 50 degrees.
Note the intersection of the 3dB circle is at approximately + & – 25 degrees for a total beamwidth of 50 degrees.
Figure E9-1

## Slide 21: Amateur Radio Extra Class Antennas
E9B03… In the antenna radiation pattern shown in Figure E9-1, the front-to-back ratio is 18 dB.
Figure E9-1
Rear lobe is half way between the -12dB and the -24dB points.

## Slide 22: Amateur Radio Extra Class Antennas
E9B04… In the antenna radiation pattern shown in Figure E9-1, the front-to-side ratio is 14 dB.
Figure E9-1
Side lobes
14 dB

## Slide 23: Amateur Radio Extra Class Antennas
E9B05… When a directional antenna is operated at different frequencies within the band for which it was designed the gain may exhibit significant variations.
E9B06… If a Yagi antenna is designed solely for maximum forward gain the front-to-back ratio decreases.
E9B07… If the boom of a Yagi antenna is lengthened and the elements are properly retuned, usually the gain increases.
Element spacing affects bandwidth response
Boom length influences gain

## Slide 24: Amateur Radio Extra Class Antennas
E9B08… The total amount of radiation emitted by a directional (gain) antenna compared with the total amount of radiation emitted from an isotropic antenna will be the same when each is driven by the same amount of power. There will be no difference in total radiated power between the two antennas.
Remember the key word is total power.
In an isotropic antenna power is equally radiated in all directions.
In a gain antenna the power is focused in one direction so in that direction it is stronger but in other directions it is weaker.
Total power is the sum of all power in all directions assuming both antennas are 100% efficient.

## Slide 25: Amateur Radio Extra Class Antennas
E3C07… The radiation pattern of a 3-element, horizontally polarized beam antenna will vary with height above ground. The main lobe takeoff angle will decrease with increasing height.
E3C10… The performance of a horizontally polarized antenna mounted on the side of a hill when compared with the same antenna mounted on flat ground will have a main lobe takeoff angle that decreases in the downhill direction.
Antenna
Antenna
Radiation Pattern
Distorted Radiation Pattern

## Slide 26: Amateur Radio Extra Class Antennas
E9C08… An antenna elevation pattern over real ground is shown in Figure E9-2.
E9C09… The elevation angle of peak response in the antenna radiation pattern shown in Figure E9-2 is 7.5 degrees.
Figure E9-2
Figure E9-2
7.5 degrees

## Slide 27: Amateur Radio Extra Class Antennas
E9C10… The front-to-back ratio of the radiation pattern shown in Figure E9-2 is 28 dB.
E9C11… Four elevation lobes appear in the forward direction of the antenna radiation pattern shown in Figure E9-2.
Figure E9-2
Back lobes
Front lobes
Four elevation lobes
Figure E9-2

## Slide 28: Amateur Radio Extra Class Antennas
E9C14… The electric field will be horizontally oriented for a Yagi with three elements mounted parallel to the ground.
E9D02… One way to produce circular polarization, when using linearly polarized antennas, is to arrange two Yagi antennas perpendicular to each other with the driven elements at the same point on the boom and fed 90 degrees out of phase.

## Slide 29: Element 4 Extra Class Question Pool
Valid July 1, 2008
Through
June 30, 2012
Antennas

## Slide 30: E9A16 What is meant by the radiation resistance of an antenna?
The combined losses of the antenna elements and feed line
The specific impedance of the antenna
The value of a resistance that would dissipate the same amount of power as that radiated from an antenna
The resistance in the atmosphere that an antenna must overcome to be able to radiate a signal

## Slide 31: E9A05 Which of the following factors determine the radiation resistance of an antenna?
Transmission-line length and antenna height
Antenna height and conductor length/diameter ratio, and location of nearby conductive objects
It is a physical constant and is the same for all antennas
Sunspot activity and time of day

## Slide 32: E9A06 What is the term for the ratio of the radiation resistance of an antenna to the total resistance of the system?
Effective radiated power
Radiation conversion loss
Antenna efficiency
Beamwidth

## Slide 33: E9A07 What is included in the total resistance of an antenna system?
Radiation resistance plus space impedance
Radiation resistance plus transmission resistance
Transmission-line resistance plus radiation resistance
Radiation resistance plus ohmic resistance

## Slide 34: E9A11 How is antenna efficiency calculated?
(radiation resistance / transmission resistance) x 100%
(radiation resistance / total resistance) x 100%
(total resistance / radiation resistance) x 100%
(effective radiated power / transmitter output) x 100%

## Slide 35: E9B01 What determines the free-space polarization of an antenna?
The orientation of its magnetic field (H Field)
The orientation of its free-space characteristic impedance
The orientation of its electric field (E Field)
Its elevation pattern

## Slide 36: E9A12 How can the efficiency of an HF quarter-wave grounded vertical antenna be improved?
By installing a good radial system
By isolating the coax shield from ground
By shortening the vertical
By reducing the diameter of the radiating element

## Slide 37: E9A13 Which is the most important factor that determines ground losses for a ground-mounted vertical antenna operating in the 3-30 MHz range?
The standing-wave ratio
Base current
Soil conductivity
Base impedance

## Slide 38: E9C15 What strongly affects the shape of the far-field, low-angle elevation pattern of a vertically polarized antenna?
The conductivity and dielectric constant of the soil in the area of the antenna
The radiation resistance of the antenna and matching network
The SWR on the transmission line
The transmitter output power

## Slide 39: E9C12 How is the far-field elevation pattern of a vertically polarized antenna affected by being mounted over seawater versus rocky ground?
The low-angle radiation decreases
The high-angle radiation increases
Both the high- and low-angle radiation decrease
The low-angle radiation increases

## Slide 40: E9C17 What is the main effect of placing a vertical antenna over an imperfect ground?
It causes increased SWR
It changes the impedance angle of the matching network
It reduces low-angle radiation
It reduces losses in the radiating portion of the antenna

## Slide 41: E9D14 Which of the following types of conductor would be best for minimizing losses in a station's RF ground system?
A resistive wire, such as a spark-plug wire
A thin, flat copper strap several inches wide
A cable with 6 or 7 18-gauge conductors in parallel
A single 12 or 10 gauge stainless steel wire

## Slide 42: E9D15 Which of these choices would provide the best RF ground for your station?
A 50-ohm resistor connected to ground
A connection to a metal water pipe
A connection to 3 or 4 interconnected ground rods driven into the Earth
A connection to 3 or 4 interconnected ground rods via a series RF choke

## Slide 43: E9C01 What is the radiation pattern of two 1/4-wavelength vertical antennas spaced 1/2-wavelength apart and fed 180 degrees out of phase?
A cardioid
Omnidirectional
A figure-8 broadside to the axis of the array
A figure-8 oriented along the axis of the array

## Slide 44: E9C02 What is the radiation pattern of two 1/4-wavelength vertical antennas spaced 1/4-wavelength apart and fed 90 degrees out of phase?
A cardioid
A figure-8 end-fire along the axis of the array
A figure-8 broadside to the axis of the array
Omnidirectional

## Slide 45: E9C03 What is the radiation pattern of two 1/4-wavelength vertical antennas spaced 1/2-wavelength apart and fed in phase?
Omnidirectional
A cardioid
A Figure-8 broadside to the axis of the array
A Figure-8 end-fire along the axis of the array

## Slide 46: E9A08 What is a folded dipole antenna?
A dipole one-quarter wavelength long
A type of ground-plane antenna
A dipole constructed from one wavelength of wire forming a very thin loop
A hypothetical antenna used in theoretical discussions to replace the radiation resistance

## Slide 47: E9D10 What is the approximate feed-point impedance at the center of a folded dipole antenna?
300 ohms
72 ohms
50 ohms
450 ohms

## Slide 48: E9A04 Why would one need to know the feed point impedance of an antenna?
To match impedances for maximum power transfer from a feed line
To measure the near-field radiation density from a transmitting antenna
To calculate the front-to-side ratio of the antenna
To calculate the front-to-back ratio of the antenna

## Slide 49: E9A01 Which of the following describes an isotropic Antenna?
A grounded antenna used to measure earth conductivity
A horizontal antenna used to compare Yagi antennas
A theoretical antenna used as a reference for antenna gain
A spacecraft antenna used to direct signals toward the earth

## Slide 50: E9A03 Which of the following antennas has no gain in any direction?
Quarter-wave vertical
Yagi
Half-wave dipole
Isotropic antenna

## Slide 51: E9A02 How much gain does a 1/2-wavelength dipole have compared to an isotropic antenna?
1.55 dB
2.15 dB
3.05 dB
4.30 dB

## Slide 52: E9A14 How much gain does an antenna have over a 1/2-wavelength dipole when it has 6 dB gain over an isotropic antenna?
3.85 dB
6.0 dB
8.15 dB
2.79 dB

## Slide 53: E9A15 How much gain does an antenna have over a 1/2-wavelength dipole when it has 12 dB gain over an isotropic antenna?
6.17 dB
9.85 dB
12.5 dB
14.15 dB

## Slide 54: E9D11 Why is a loading coil often used with an HF mobile antenna?
To improve reception
To lower the losses
To lower the Q
To cancel capacitive reactance

## Slide 55: E9D08 What happens to the bandwidth of an antenna as it is shortened through the use of loading coils?
It is increased
It is decreased
No change occurs
It becomes flat

## Slide 56: E9A10 What is meant by antenna bandwidth?
Antenna length divided by the number of elements
The frequency range over which an antenna satisfies a performance requirement
The angle between the half-power radiation points
The angle formed between two imaginary lines drawn through the element ends

## Slide 57: E9D06 Why should an HF mobile antenna loading coil have a high ratio of reactance to resistance?
To swamp out harmonics
To maximize losses
To minimize losses
To minimize the Q

## Slide 58: E9D05 For a shortened vertical antenna, where should a loading coil be placed to minimize losses and produce the most effective performance?
Near the center of the vertical radiator
As low as possible on the vertical radiator
As close to the transmitter as possible
At a voltage node

## Slide 59: E9D09 What is an advantage of using top loading in a shortened HF vertical antenna?
Lower Q
Greater structural strength
Higher losses
Improved radiation efficiency

## Slide 60: E9D13 What happens at the base feed-point of a fixed-length HF mobile antenna as the frequency of operation is lowered?
The resistance decreases and the capacitive reactance decreases
The resistance decreases and the capacitive reactance increases
The resistance increases and the capacitive reactance decreases
The resistance increases and the capacitive reactance increases

## Slide 61: E9D12 What is an advantage of using a trapped antenna?
It has high directivity in the higher-frequency bands
It has high gain
It minimizes harmonic radiation
It may be used for multi-band operation

## Slide 62: E9D07 What is a disadvantage of using a multi-band trapped antenna?
It might radiate harmonics
It can only be used for single-band operation
It is too sharply directional at lower frequencies
It must be neutralized

## Slide 63: E9B09 How can the approximate beamwidth of a directional antenna be determined?
Note the two points where the signal strength of the antenna is 3 dB less than maximum and compute the angular difference
Measure the ratio of the signal strengths of the radiated power lobes from the front and rear of the antenna
Draw two imaginary lines through the ends of the elements and measure the angle between the lines
Measure the ratio of the signal strengths of the radiated power lobes from the front and side of the antenna

## Slide 64: E9B10 What type of computer program technique is commonly used for modeling antennas?
Graphical analysis
Method of Moments
Mutual impedance analysis
Calculus differentiation with respect to physical properties

## Slide 65: E9B14 What does the abbreviation NEC stand for when applied to antenna modeling programs?
Next Element Comparison
Numerical Electromagnetics Code
National Electrical Code
Numeric Electrical Computation

## Slide 66: E9B13 Which of the following is a disadvantage of NEC-based antenna modeling programs?
They can only be used for simple wire antennas
They are not capable of generating both vertical and horizontal polarization patterns
Computing time increases as the number of wire segments is increased
All of these answers are correct

## Slide 67: E9B12 What is a disadvantage of decreasing the number of wire segments in an antenna model below the guideline of 10 segments per half-wavelength?
Ground conductivity will not be accurately modeled
The resulting design will favor radiation of harmonic energy
The computed feed-point impedance may be incorrect
The antenna will become mechanically unstable

## Slide 68: E9B15 What type of information can be obtained by submitting the details of a proposed new antenna to a modeling program?
SWR vs. frequency charts
Polar plots of the far-field elevation and azimuth patterns
Antenna gain
All of these answers are correct

## Slide 69: E0A01 What, if any, are the differences between the radiation produced by radioactive materials and the electromagnetic energy radiated by an antenna?
There is no significant difference between the two types of radiation
Only radiation produced by radioactivity can injure human beings
RF radiation does not have sufficient energy to break apart atoms and molecules; radiation from radioactive sources does
Radiation from an antenna will damage unexposed photographic film, ordinary radioactive materials do not cause this problem

## Slide 70: E0A09 Which insulating material commonly used as a thermal conductor for some types of electronic devices is extremely toxic if broken or crushed and the particles are accidentally inhaled?
Mica
Zinc oxide
Beryllium Oxide
Uranium Hexaflouride

## Slide 71: E9B11 What is the principle of a Method of Moments analysis?
A wire is modeled as a series of segments, each having a distinct value of current
A wire is modeled as a single sine-wave current generator
A wire is modeled as a series of points, each having a distinct location in space
A wire is modeled as a series of segments, each having a distinct value of voltage across it

## Slide 72: E9A09 What is meant by antenna gain?
The numerical ratio relating the radiated signal strength of an antenna in the direction of maximum radiation to that of a reference antenna
The numerical ratio of the signal in the forward direction to that in the opposite direction
The ratio of the amount of power radiated by an antenna compared to the transmitter output power
The final amplifier gain minus the transmission-line losses (including any phasing lines present)

## Slide 73: E0A07 What is the "far-field" zone of an antenna?
The area of the ionosphere where radiated power is not refracted
The area where radiated power dissipates over a specified time period
The area where radiated field strengths are obstructed by objects of reflection
The area where the shape of the antenna pattern is independent of distance

## Slide 74: E9B02 In the antenna radiation pattern shown in Figure E9-1, what is the 3-dB beamwidth?
75 degrees
50 degrees
25 degrees
30 degrees
Notes: <number>

## Slide 75: E9B03 In the antenna radiation pattern shown in Figure E9-1, what is the front-to-back ratio?
36 dB
18 dB
24 dB
14 dB

## Slide 76: E9B04 In the antenna radiation pattern shown in Figure E9-1, what is the front-to-side ratio?
12 dB
14 dB
18 dB
24 dB

## Slide 77: E9B05 What may occur when a directional antenna is operated at different frequencies within the band for which it was designed?
Feed-point impedance may become negative
The E-field and H-field patterns may reverse
Element spacing limits could be exceeded
The gain may exhibit significant variations

## Slide 78: E9B06 What usually occurs if a Yagi antenna is designed solely for maximum forward gain?
The front-to-back ratio increases
The front-to-back ratio decreases
The frequency response is widened over the whole frequency band
The SWR is reduced

## Slide 79: E9B07 If the boom of a Yagi antenna is lengthened and the elements are properly retuned, what usually occurs?
The gain increases
The SWR decreases
The front-to-back ratio increases
The gain bandwidth decreases rapidly

## Slide 80: E9B08 How does the total amount of radiation emitted by a directional (gain) antenna compare with the total amount of radiation emitted from an isotropic antenna, assuming each is driven by the same amount of power?
The total amount of radiation from the directional antenna is increased by the gain of the antenna
The total amount of radiation from the directional antenna is stronger by its front to back ratio
There is no difference between the two antennas
The radiation from the isotropic antenna is 2.15 dB stronger than that from the directional antenna

## Slide 81: E3C07 How does the radiation pattern of a 3-element, horizontally polarized beam antenna vary with height above ground?
The main lobe takeoff angle increases with increasing height
The main lobe takeoff angle decreases with increasing height
The horizontal beam width increases with height
The horizontal beam width decreases with height

## Slide 82: E3C10 How does the performance of a horizontally polarized antenna mounted on the side of a hill compare with the same antenna mounted on flat ground?
The main lobe takeoff angle increases in the downhill direction
The main lobe takeoff angle decreases in the downhill direction
The horizontal beam width decreases in the downhill direction
The horizontal beam width increases in the uphill direction

## Slide 83: E9C08 What type of antenna pattern over real ground is shown in Figure E9-2?
Elevation
Azimuth
Radiation resistance
Polarization

## Slide 84: E9C09 What is the elevation angle of peak response in the antenna radiation pattern shown in Figure E9-2?
45 degrees
75 degrees
7.5 degrees
25 degrees

## Slide 85: E9C10 What is the front-to-back ratio of the radiation pattern shown in Figure E9-2?
15 dB
28 dB
3 dB
24 dB

## Slide 86: E9C11 How many elevation lobes appear in the forward direction of the antenna radiation pattern shown in Figure E9-2?
4
3
1
7

## Slide 87: E9C14 How would the electric field be oriented for a Yagi with three elements mounted parallel to the ground?
Vertically
Horizontally
Right-hand elliptically
Left-hand elliptically

## Slide 88: E9D02 What is one way to produce circular polarization when using linearly polarized antennas?
Stack two Yagis, fed 90 degrees out of phase, to form an array with the respective elements in parallel planes
Stack two Yagis, fed in phase, to form an array with the respective elements in parallel planes
Arrange two Yagis perpendicular to each other with the driven elements at the same point on the boom and fed 90 degrees out of phase
Arrange two Yagis collinear to each other, with the driven elements fed 180 degrees out of phase