## Slide 1: Amateur Extra Licensing Class
Presented by
W5YI
Arlington, Texas
Skywaves & Contesting
Notes: <number>

## Slide 2: Amateur Radio Extra Class Element 4 Course Presentation
ELEMENT 4 Groupings
  Rules & Regs
  Skywaves & Contesting
  Outer Space Comms
  Visuals & Video Modes
  Digital Excitement with Computers & Radios
  Modulate Your Transmitters
  Amps & Power Supplies
  Receivers with Great Filters

## Slide 3: Amateur Radio Extra Class Element 4 Course Presentation
ELEMENT 4 Groupings
  Oscillate & Synthesize This!
  Circuits & Resonance for All!
  Components in Your New Rig
  Logically Speaking of Counters
  Optos & OpAmps Plus Solar
  Test Gear, Testing, Testing 1,2,3
  Antennas
  Feedlines & Safety

## Slide 4: Amateur Radio Extra Class Skywaves & Contesting
E8D07… An electromagnetic wave is a wave consisting of an electric field and a magnetic field oscillating at right angles to each other.
Radiation Pattern of Radio Waves Around Antenna

## Slide 5: Amateur Radio Extra Class Skywaves & Contesting
E8D08… Electromagnetic waves traveling in free space change electric and magnetic fields to propagate the energy.
E8D10… The polarization of an electromagnetic wave when its magnetic field is parallel to the surface of the earth is vertical.
E8D11… The polarization of an electromagnetic wave if its magnetic field is perpendicular to the surface of the Earth is Horizontal.
Vertically-Polarized Antenna
Horizizontally-Polarized Antenna

## Slide 6: Amateur Radio Extra Class Skywaves & Contesting
E8D09… Circularly polarized electromagnetic waves are waves with a rotating electric field.
E8D12… Electromagnetic waves travel in free space at approximately 300 million meters per second. (not miles per second)
E3B04… Long-path propagation is probably occurring if an HF beam antenna is pointed in a direction 180 degrees away from a station in order to receive the strongest signals.
E3B05… The 160 to 10 meter amateur bands typically support long-path propagation.
E3B06… The 20 meter amateur band most frequently provides long-path propagation.
E3B07… Receipt of a signal by more than one path could account for hearing an echo on the received signal of a distant station.

## Slide 7: Amateur Radio Extra Class Skywaves & Contesting
E3C08… The name of the high-angle wave in HF propagation that travels for some distance within the F2 region is the Pedersen ray.
  Paths 4 and 5 are Pedersen rays or high-angle rays. These rays are not refracted sufficiently to return directly to the earth but don't have a high enough angle to penetrate (like ray 6). They get trapped in the ionosphere often exiting where there is a big gradient in electron density (at dusk and dawn).

## Slide 8: Amateur Radio Extra Class Skywaves & Contesting
E2C12… In North America during low sunspot activity, when signals from Europe become weak and fluttery across an entire HF band two to three hours after sunset, it might help to switch to a lower frequency HF band in order to contact other European DX stations.
E3B08… Gray-line propagation is probably occurring if radio signals travel along the terminator between daylight and darkness.

## Slide 9: Amateur Radio Extra Class Skywaves & Contesting
E3B10… The cause of gray-line propagation is at twilight, solar absorption drops greatly, while atmospheric ionization is not weakened enough to reduce the MUF.
  During twilight, the D layer quickly disappears resulting in less absorption, while the E and F layers continue relatively strong.
  This also happens during solar eclipses
E3B11… Contacts up to 8,000 to 10,000 miles on three or four HF bands are possible during gray-line propagation.
E3B09… Gray-line propagation is most prevalent at sunrise and sunset.
  A gray-line communications path, by definition, follows the daylight/dark “terminator” whenever it happens to exist at any given moment.
  This means that the communications path involved with gray-line propagation is constrained within the boundaries of the gray-line.

## Slide 10: Amateur Radio Extra Class Skywaves & Contesting
E3A09… When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at the E layer of the ionosphere.
E3A10… The 28 - 148 MHz range of frequencies is well suited for meteor-scatter communications.
E3A11… Transmit and receive time sequencing of 15-second sequences, where one station transmits for 15 seconds and then receives for the following 15 seconds is normally used on 144 MHz when attempting a meteor-scatter contact.

## Slide 11: Amateur Radio Extra Class Skywaves & Contesting
  E3B01… Transequatorial propagation is propagation between two points at approximately the same distance north and south of the magnetic equator.

## Slide 12: Amateur Radio Extra Class Skywaves & Contesting
  The characteristics of TEP (Trans Equatorial Propagation):
  It is thought that TEP arises when there is an increased level of ionization in equatorial regions.
  This enables signals that enter the ionosphere at the correct angle to be propagated across the equator.
  In view of the way in which the signals are propagated they must enter the ionosphere virtually in a north south direction, otherwise propagation does not occur.
  It is also found that signals undergo two reflections by the ionosphere before they are returned to earth.

## Slide 13: Amateur Radio Extra Class Skywaves & Contesting
E3B02… The approximate maximum range for signals using transequatorial propagation is 2500 miles.
  The maximum total distance for a TE contact is 5000 miles.
E3B03… Afternoon or early evening is the best time of day for transequatorial propagation.
E3C01… Auroral activity causes radio communication of CW signals to have a fluttery tone.
E3C02… The cause of auroral activity is the emission of charged particles from the sun.
A magnetic filament erupted and hurled a massive coronal mass ejection (CME) off the sun's northwestern limb. (9/4/2010)

## Slide 14: Amateur Radio Extra Class Skywaves & Contesting
E3C03… Auroral activity in the ionosphere occurs at E-region height.
Lake Michigan
Seattle, WA

## Slide 15: Amateur Radio Extra Class Skywaves & Contesting
E3C04… The CW emission mode is best for auroral propagation.
E3C11… From within the contiguous 48 states, an antenna should be pointed approximately north to take maximum advantage of auroral propagation.
E3C05… Selective fading is caused by phase differences in the received signal caused by different paths.

## Slide 16: Amateur Radio Extra Class Skywaves & Contesting
E4E06… Thunderstorms are a major cause of atmospheric static.
E3C14… Because Radio waves may be bent, the radio-path horizon distance can exceed the geometric horizon (by about 15%).
      VHF & UHF radio signals will generally travel “line of sight.”
      VHF & UHF radio signals are blocked by the curvature of the Earth.

## Slide 17: Amateur Radio Extra Class Skywaves & Contesting
E3C06… VHF/UHF radio-path horizon distance exceeds the geometric horizon by approximately 15% of the distance.
Depending on local weather conditions, a 15% to 30% range enhancement over the optical horizon will usually take place at VHF and UHF radio frequency bands.
Radio waves bend slightly over the horizon because of the difference in the air’s refractive index at higher altitudes.

## Slide 18: Amateur Radio Extra Class Skywaves & Contesting
E3C09… Tropospheric ducting is usually responsible for propagating VHF signals over 500 miles.
Tropospheric Ducting

## Slide 19: Amateur Radio Extra Class Skywaves & Contesting
E3C12… As the frequency of a signal is increased, its ground wave propagation decreases.
  Ground waves travel further on lower frequencies, so as the frequency of a signal is increased, ground wave propagation is decreased.
  Fog horns always blast out a very low audio tone due to this condition.
E3C13… Most ground-wave propagation has a Vertical polarization.

## Slide 20: Amateur Radio Extra Class Skywaves & Contesting
E2C01… Operators are permitted to make contacts even if they do not submit a log when operating a contest.
E2C05… 14.310 MHz would generally be acceptable for U.S. stations to work other U.S. stations in a phone contest.
  5405 kHz (middle of 60 meter band), 50.050 MHz (CW portion of 6 meters) and 146.52 MHz (national calling frequency) would generally not be acceptable for U.S. stations to work other U.S. stations in a phone contest
E2C11… You generally sign your full call sign once or twice when attempting to contact a DX station working a “pileup” or in a contest.

## Slide 21: Amateur Radio Extra Class Skywaves & Contesting
E2C10… A phone DX station might state that he or she is listening on another frequency for one or more reasons such as:
  Because the DX station may be transmitting on a frequency that is prohibited to some responding stations.
  To separate the calling stations from the DX station.
  To reduce interference, thereby improving operating efficiency.
E2C07… The Cabrillo format is a standard for organizing information in contest log files.
  http://www.cqwpx.com/cabrillo.htm for the Cabrillo Format.
E2C02… The generally prohibited practice of posting one’s own call sign and frequency on a call sign spotting network is described as “self spotting” in regards to contest operation.

## Slide 22: Amateur Radio Extra Class Skywaves & Contesting
E2C06… During a VHF/UHF contest you would expect to find the highest level of activity in the weak signal segment of the band, with most of the activity near the calling frequency.
E2C04… An amateur radio contest contact is generally discouraged on 146.52 MHz
  The national 2 meter calling frequency.
E2C03… Amateur radio contesting is generally excluded on 30 meters.
Band Calling Frequency
6 meters 50.125 MHz
2 meters 144.200 MHz
1.25 222.1 MHz
70 cm 432.100 MHz
35 cm 902.100 MHz
23 cm 1296.100 MHz

## Slide 23: Element 4 Extra Class Question Pool Skywaves & Contesting
Valid July 1, 2008
Through
June 30, 2012

## Slide 24: E8D07 What is an electromagnetic wave?
  Alternating currents in the core of an electromagnet
  A wave consisting of two electric fields at right angles to each other
  A wave consisting of an electric field and a magnetic field oscillating at right angles to each other
  A wave consisting of two magnetic fields at right angles to each other

## Slide 25: E8D08 Which of the following best describes electromagnetic waves traveling in free space?
  Electric and magnetic fields become aligned as they travel
  The energy propagates through a medium with a high refractive index
  The waves are reflected by the ionosphere and return to their source
  Changing electric and magnetic fields propagate the energy

## Slide 26: E8D10 What is the polarization of an electromagnetic wave if its magnetic field is parallel to the surface of the Earth?
  Circular
  Horizontal
  Elliptical
  Vertical

## Slide 27: E8D11 What is the polarization of an electromagnetic wave if its magnetic field is perpendicular to the surface of the Earth?
  Horizontal
  Circular
  Elliptical
  Vertical

## Slide 28: E8D09 What is meant by circularly polarized electromagnetic waves?
  Waves with an electric field bent into a circular shape
  Waves with a rotating electric field
  Waves that circle the Earth
  Waves produced by a loop antenna

## Slide 29: E8D12 At approximately what speed do electromagnetic waves travel in free space?
  300 million meters per second
  186,300 meters per second
  186,300 feet per second
  300 million miles per second

## Slide 30: E3B04 What type of propagation is probably occurring if an HF beam antenna must be pointed in a direction 180 degrees away from a station to receive the strongest signals?
  Long-path
  Sporadic-E
  Transequatorial
  Auroral

## Slide 31: E3B05 Which amateur bands typically support long-path propagation?
  160 to 40 meters
  30 to 10 meters
  160 to 10 meters
  6 meters to 2 meters

## Slide 32: E3B06 Which of the following amateur bands most frequently provides long-path propagation?
  80 meters
  20 meters
  10 meters
  6 meters

## Slide 33: E3B07 Which of the following could account for hearing an echo on the received signal of a distant station?
  High D layer absorption
  Meteor scatter
  Transmit frequency is higher than the MUF
  Receipt of a signal by more than one path

## Slide 34: E3C08 What is the name of the high-angle wave in HF propagation that travels for some distance within the F2 region?
  Oblique-angle ray
  Pedersen ray
  Ordinary ray
  Heaviside ray

## Slide 35: E2C12 In North America during low sunspot activity, when signals from Europe become weak and fluttery across an entire HF band two to three hours after sunset, what might help to contact other European DX stations?
  Switch to a higher frequency HF band
  Switch to a lower frequency HF band
  Wait 90 minutes or so for the signal degradation to pass
  Wait 24 hours before attempting another communication on the band

## Slide 36: E3B08 What type of propagation is probably occurring if radio signals travel along the terminator between daylight and darkness?
  Transequatorial
  Sporadic-E
  Long-path
  Gray-line

## Slide 37: E3B10 What is the cause of gray-line propagation?
  At midday, the sun, being directly overhead, superheats the ionosphere causing increased refraction of radio waves
  At twilight, solar absorption drops greatly, while atmospheric ionization is not weakened enough to reduce the MUF
  At darkness, solar absorption drops greatly, while atmospheric ionization remains steady
  At mid afternoon, the sun heats the ionosphere, increasing radio wave refraction and the MUF

## Slide 38: E3B11 What communications are possible during gray-line propagation?
  Contacts up to 2,000 miles only on the 10-meter band
  Contacts up to 750 miles on the 6- and 2-meter bands
  Contacts up to 8,000 to 10,000 miles on three or four HF bands
  Contacts up to 12,000 to 15,000 miles on the 2 meter and 70 centimeter bands

## Slide 39: E3B09 At what time of day is gray-line propagation most prevalent?
  At sunrise and sunset
  When the sun is directly above the location of the transmitting station
  When the sun is directly overhead at the middle of the communications path between the two stations
  When the sun is directly above the location of the receiving station

## Slide 40: E3A09 When a meteor strikes the Earth's atmosphere, a cylindrical region of free electrons is formed at what layer of the ionosphere?
  The E layer
  The F1 layer
  The F2 layer
  The D layer

## Slide 41: E3A10 Which range of frequencies is well suited for meteor-scatter communications?
  1.8 - 1.9 MHz
  10 - 14 MHz
  28 - 148 MHz
  220 - 450 MHz

## Slide 42: E3A11 What transmit and receive time sequencing is normally used on 144 MHz when attempting a meteor-scatter contact?
  Two-minute sequences, where one station transmits for a full two minutes and then receives for the following two minutes
  One-minute sequences, where one station transmits for one minute and then receives for the following one minute
  15-second sequences, where one station transmits for 15 seconds and then receives for the following 15 seconds
  30-second sequences, where one station transmits for 30 seconds and then receives for the following 30 seconds

## Slide 43: E3B01 What is transequatorial propagation?
  Propagation between two points at approximately the same distance north and south of the magnetic equator
  Propagation between any two points located on the magnetic equator
  Propagation between two continents by way of ducts along the magnetic equator
  Propagation between two stations at the same latitude

## Slide 44: E3B02 What is the approximate maximum range for signals using transequatorial propagation?
  1000 miles
  2500 miles
  5000 miles
  7500 miles

## Slide 45: E3B03 What is the best time of day for transequatorial propagation?
  Morning
  Noon
  Afternoon or early evening
  Late at night

## Slide 46: E3C01 What effect does auroral activity have on radio communications?
  Signals experience long-delay echo
  FM communications are clearer
  CW signals have a clearer tone
  CW signals have a fluttery tone

## Slide 47: E3C02 What is the cause of auroral activity?
  Reflections in the solar wind
  A low sunspot level
  The emission of charged particles from the sun
  Meteor showers concentrated in the northern latitudes

## Slide 48: E3C03 Where in the ionosphere does auroral activity occur?
  At F-region height
  In the equatorial band
  At D-region height
  At E-region height

## Slide 49: E3C04 Which emission mode is best for auroral propagation?
  CW
  SSB
  FM
  RTTY

## Slide 50: E3C11 From the contiguous 48 states, in which approximate direction should an antenna be pointed to take maximum advantage of auroral propagation?
  South
  North
  East
  West

## Slide 51: E3C05 What causes selective fading?
  Small changes in beam heading at the receiving station
  Phase differences in the received signal caused by different paths
  Large changes in the height of the ionosphere
  Time differences between the receiving and transmitting stations

## Slide 52: E4E06 What is a major cause of atmospheric static?
  Solar radio frequency emissions
  Thunderstorms
  Geomagnetic storms
  Meteor showers

## Slide 53: E3C14 Why does the radio-path horizon distance exceed the geometric horizon?
  E-region skip
  D-region skip
  Auroral skip
  Radio waves may be bent

## Slide 54: E3C06 How much farther does the VHF/UHF radio-path horizon distance exceed the geometric horizon?
  By approximately 15% of the distance
  By approximately twice the distance
  By approximately one-half the distance
  By approximately four times the distance

## Slide 55: E3C09 What effect is usually responsible for propagating a VHF signal over 500 miles?
  D-region absorption
  Faraday rotation
  Tropospheric ducting
  Moonbounce

## Slide 56: E3C12 As the frequency of a signal is increased, how does its ground wave propagation change?
  It increases
  It decreases
  It stays the same
  Radio waves don't propagate along the Earth's surface

## Slide 57: E3C13 What type of polarization does most ground-wave propagation have?
  Vertical
  Horizontal
  Circular
  Elliptical

## Slide 58: E2C01 Which of the following is true about contest operating?
  Operators are permitted to make contacts even if they do not submit a log
  Interference to other amateurs is unavoidable and therefore acceptable
  It is mandatory to transmit the call sign of the station being worked as part of every transmission to that station
  Every contest requires a signal report in the exchange

## Slide 59: E2C05 Which of the following frequencies would generally be acceptable for U.S. stations to work other U.S. stations in a phone contest?
  5405 kHz
  14.310 MHz
  50.050 MHz
  146.52 MHz

## Slide 60: E2C11 How should you generally sign your call when attempting to contact a DX station working a “pileup” or in a contest?
Send your full call sign once or twice
Send only the last two letters of your call sign until you make contact
Send your full call sign and grid square
Send the call sign of the DX station three times, the words "this is", then your call sign three times

## Slide 61: E2C10 Why might a phone DX station state that he is listening on another frequency?
  Because the DX station may be transmitting on a frequency that is prohibited to some responding stations
  To separate the calling stations from the DX station
  To reduce interference, thereby improving operating efficiency
  All of these choices are correct

## Slide 62: E2C07 What is the Cabrillo format?
  A standard for organizing information in contest log files
  A method of exchanging information during a contest QSO
  The most common set of contest rules
  The rules of order for meetings between contest sponsors

## Slide 63: E2C02 Which of the following best describes “self spotting” in regards to contest operating?
  The generally prohibited practice of posting one’s own call sign and frequency on a call sign spotting network
  The acceptable practice of manually posting the call signs of stations on a call sign spotting network
  A manual technique for rapidly zero beating or tuning to a station’s frequency before calling that station
  An automatic method for rapidly zero beating or tuning to a station’s frequency before calling that station

## Slide 64: E2C06 During a VHF/UHF contest, in which band segment would you expect to find the highest level of activity?
At the top of each band, usually in a segment reserved for contests
In the middle of each band, usually on the national calling frequency
In the weak signal segment of the band, with most of the activity near the calling frequency
In the middle of the band, usually 25 kHz above the national calling frequency

## Slide 65: E2C04 On which of the following frequencies is an amateur radio contest contact generally discouraged?
  3.525 MHz
  14.020 MHz
  28.330 MHz
  146.52 MHz

## Slide 66: E2C03 From which of the following bands is amateur radio contesting generally excluded?
  30 meters
  6 meters
  2 meters
  33 cm